## Slide 1: Case Studies in Process Design II Clemens Isert, Selina Schlotterbeck, Tobias Seidler, Mithurshan Tharmalingam, Pauline Oeuvray

## Slide 2: Reactor flow sheet

## Slide 3: Made assumptions for the HCN absorber
Ideal case
Isothermal column
Heat of absorption neglected
Outlet temperature same for gas and liquid
Only HCN is absorbed
Heat capacities not temperature dependent
No HCN in liquid inlet stream
Resistivity in the liquid phase neglected
Non-ideal case
Isothermal column
Heat of absorption neglected
Outlet temperature same for gas and liquid
Only HCN is absorbed

## Slide 4: Sensitivity analysis of the HCN Absorber
Height of the column increases with decreasing inlet liquid flow
Better absorption
CAPEX decreases
OPEX increases

## Slide 5: Results
Reactor:
Ideal vs. real (case 1/case 3)
  Length: 12 m / 28 m
  Number of tubes: 1’342 / 17’149
Co- vs. counter-current (case 3/case 4)
  Number of tubes: 17’149 / 40’642
  Heating medium flow: 0.10 / 0.05
  Conversion CH4: 0.82 / 0.59

## Slide 6: Results
NH3 absorber:
Ideal vs. real (case 1/case 3)
  Column height: 2.44 m / 4.39 m
  Diameter: 0.79 m / 0.79 m
  Flow rate ratio 0.80 / 1.64
  Temperature in the column
  Volumetric fraction H2SO4 : 0.37 / 2.01

## Slide 7: Results
HCN absorber:
Ideal vs. real (case 1/case 3)
  Column height: 9.73 m / 10.31 m
  Diameter: 1.11 m / 1.10 m
  Outlet temperature: 294.72 K / 293.57 K
  Water

## Slide 8: Results
HCN distillation:
Ideal vs. real (case 1/case 3)
  Column height: 9.36 m / 10.08 m
  Diameter: 1.73 m / 1.92 m
  Heat exchanger area: 0.057 m2 / 0.056 m2

## Slide 9: Results
Costs
Ideal vs. real (case 1/case 3)
  Break-even price: 0.62 $/kg / 0.76 $/kg

## Slide 16: Contact information and credits
ETH Zurich
Organisational unit
Street address
Postcode City
www.ethz.ch/en.html
Publisher: Organisational unit of ETH Zurich
Design: Designer Name
Images: Credit (slide xx), Credit (slide xx)
© ETH Zurich, December 2013