## Slide 1: Case Studies in Process Design II Clemens Isert, Selina Schlotterbeck, Tobias Seidler, Mithurshan Tharmalingam, Pauline Oeuvray

## Slide 2: Reactor flow sheet

## Slide 3: General Modelling Approach
Four cases considered:
Overall optimization with a “black box” approach
 | Case 1 | Case 2 | Case 3 | Case 4
Gas model | ideal gas law | ideal gas law | Peng-Robinson-EOS | Peng-Robinson-EOS
Heating mode | cross-current | cross-current | cross-current | co-current
Absorbers | shortcut model | shortcut model | non-ideal Eq.-model | non-ideal Eq.-model
Distillation | Fenske-Underwood-Gilliland | Fenske-Underwood-Gilliland | NRTL | NRTL
ΔP considered | no | yes | yes | yes

## Slide 4: ODE-system governing the reactor

## Slide 5
Assumptions for Ammonia Absorber
Ideal case
Heat capacities are T independent
Non ideal case
Heat capacities are T dependent
General
Isothermal column
Instantaneous & irreversible reaction
Heat of absorption neglected
Outlet temperature for liquid and gas alike
No HCN absorption in water
No pressure drop
20 % excess of sulfuric acid

## Slide 6
Sensitivity Analysis of the Ammonia Absorber

## Slide 7: Made assumptions for the HCN absorber
Ideal case
Isothermal column
Heat of absorption neglected
Outlet temperature same for gas and liquid
Only HCN is absorbed
Heat capacities not temperature dependent
No HCN in liquid inlet stream
Resistivity in the liquid phase neglected
Non-ideal case
Isothermal column
Heat of absorption neglected
Outlet temperature same for gas and liquid
Only HCN is absorbed

## Slide 8: Sensitivity analysis of the HCN Absorber
Height of the column increases with decreasing inlet liquid flow
Better absorption
CAPEX decreases
OPEX increases

## Slide 9: HCN Distillation
Ideal or non-ideal (NRTL for liquid phase)
No ΔP / ΔP
Fenkse-Underwood-Gilliland method (justified since relative volatilities were pretty similar)
xHCND = 0.995,xHCNB = 10 ppm (going below these limits only makes the separation more difficult  higher CAPEX/OPEX)
total condenser, q = 1 (requires another heat exchanger before the distillation column)

## Slide 10: Results
Reactor:
Ideal vs. real (case 1/case 3)
  Length: 12 m / 28 m
  Number of tubes: 1’342 / 17’149
Cross- vs. co-current (case 3/case 4)
  Number of tubes: 17’149 / 40’642
  Heating medium flow: 0.10 / 0.05
  Conversion CH4: 0.82 / 0.59

## Slide 11: Reactor profile case 3

## Slide 12: Results
NH3 absorber:
Ideal vs. real (case 1/case 3)
  Column height: 2.44 m / 4.39 m
  Diameter: 0.79 m / 0.79 m
  Flow rate ratio 0.80 / 1.64
  Temperature in the column
  Volumetric fraction H2SO4 : 0.37 / 2.01

## Slide 13: Results
HCN absorber:
Ideal vs. real (case 1/case 3)
  Column height: 9.73 m / 10.31 m
  Diameter: 1.11 m / 1.10 m
  Outlet temperature: 294.72 K / 293.57 K
  Water

## Slide 14: Results
HCN distillation:
Ideal vs. real (case 1/case 3)
  Column height: 9.36 m / 10.08 m
  Diameter: 1.73 m / 1.92 m
  Heat exchanger area: 0.057 m2 / 0.056 m2

## Slide 15: Results
Costs
Ideal vs. real (case 1/case 3)
  Break-even price: 0.62 $/kg / 0.76 $/kg

## Slide 22: Contact information and credits
ETH Zurich
Organisational unit
Street address
Postcode City
www.ethz.ch/en.html
Publisher: Organisational unit of ETH Zurich
Design: Designer Name
Images: Credit (slide xx), Credit (slide xx)
© ETH Zurich, December 2013